## Slide 1: Mission Planner Tutorial
Load the firmware onto boards with existing ArduPilot firmware.
Connect autopilot(pixhawk) to your computer using USB cable.
Select the COM port in mission planner software on the upper right corner.
(P.S. Do not connect it).
On mission planner , go to SETUP -> Install Firmware and select the appropriate icon that we want. Hit Yes.

## Slide 2: Connect Mission Planner to AutoPilot
Connect the Telemetry Radio, pixhawk to computer.
On mission planner, Select the desired port and data rate and then press the Connect button to connect to the autopilot. After connecting Mission Planner will download parameters from the autopilot.

## Slide 3: Hardware configuration
Frame type configuration
Accelerometer calibration
Compass calibration
Radio control calibration
RC transmitter mode setup
ESC calibration
Failsafe mechanism